## Slide 1: MADMAX Towards a Dielectric Axion Haloscope
Erika Garutti Universität Hamburg
On behalf of the MADMAX Collaboration

## Slide 2: Open Dielectric Haloscope
MADMAX:
Tunable in frequency coverage:
~10-100 GHz
Boost emitted power through:
  coherent emission from multiple interfaces
  constructive interference effects
Coupling to ga𝛾𝛾 scales with:
  external field, ∝ B
  conversion surface, ∝ A0.5
Notes: 5/4 comes from the fact, that our SNR depends on 1/sqrt(Δν) ~ 1/sqrt(m_a) since the Δν comes from the doppler broadening at the frequency of the axion mass. This then goes inversely into C_aγ^2 and in the end g_aγ ~ m_a C_aγ ~ m_a * m_a^(1/4).

## Slide 3: Open Dielectric Haloscope
axion photon coupling [GeV-1]
axion mass [eV]
Plot from https://cajohare.github.io/AxionLimits/
40 to 180 µeV (post-inflationary scenario)
cavities
dielectric haloscopes
Nat. Commun. 13, 1049 (2022) (https://doi.org/10.1038/s41467-022-28669-y)
MADMAX:
Tunable in frequency coverage:
~10-100 GHz
Corresponding to axion mass:
40-400 µeV
Coupling to ga𝛾𝛾 scales with:
  external field, ∝ B
  conversion surface, ∝ A0.5
Power boost factor:

## Slide 4: Open Dielectric Haloscope
MADMAX
baseline design
axion photon coupling [GeV-1]
axion mass [eV]
Feasibility studies
on prototype systems
Disk tiling, flatness alignment, …
Checked with MACQU
Require prototype tests in a cryostat

## Slide 5: MADMAX Magnet Update
Quench velocity
Quench propagation
Dipole Magnet most critical item for full-size MADMAX
Design for 9 T large bore conceptually very well advanced
Novel conductor: cable in copper conduit  production is feasible
Quench propagation velocity was measured in dedicated setup: MAdmax Coil for Quench Understanding  Main project risk mitigated: Quench propagation according to requirements for safe operation
Development in innovation partnership
MACQU
MACQU data
MACQU data
simulation
C. Loprin et. al
IEEE Transactions on Applied Superconductivity vol. 33 Issue 7 (2023) 1-11

## Slide 6: Staged Prototype Program
MADMAX
Many disks with large ⌀  tiled LaAlO3
Boost dish antenna emission
Closed Boosters (CB):
⌀ = 100 mm (CB100), 3 Al2O3 disks
⌀ = 200 mm (CB200), 3 Al2O3 disks
Open Boosters (OB):
⌀ = 200 mm (OB200), 2 Al2O3 disks
⌀ = 300 mm (OB300), 3 disks (Al2O3 & LaAlO3)
Aim:
First ALP run at ~19 GHz with system “easy to simulate”
Increase ALP sensitivity & understand scaling issues
 Understanding readout chain and RF behaviour
GOAL
Technical test of components (motors, interferometer, ..)
Proof-of-concept for MADMAX
 Establish boost factor calibration in an OB
Large bore (⌀ = 760 mm ) cryostat allows operation of all prototypes
Fits into the 1600 mm warm bore of MORPURGO magnet at CERN

## Slide 7: CB100: First ALP Search
Simple closed system to understand RF behaviour
Receiver
Parabolic taper
3x Ø100 mm disks (fixed distances)
Copper mirror
Closed Booster 100
DAQ system
Tested in MORPURGO
@ CERN
in 2022 and 2023

## Slide 8: CB100: First ALP Search
RF response
Boost factor extracted from model tuned to data 
Thermal noise
Boost peak
ADS simulation
2GHz SA meas.
Consistent Boost factor in 2022 and 2023
Different LNA matching impedance: 25 Ohm (2022), 30 Ohm (2023)
 Data analysis ongoing
 | Q
CB100·η | 1185
(CB100+LNA)·η | 862
(CB100+LNA)·η | 903
η = coupling efficiency of axion to system

## Slide 9: CB200: Understanding Scaling
Coupling to ga𝛾𝛾 scales with:
  conversion surface, ∝ A0.5
Larger dimensions increase the number of allowed modes
 Learn to deal with overmoded systems relevant for OB
Using a dielectric lens (Rexolite) decreases coupling of unwanted modes and allows for “quiet" regions in the spectrum
Notes: Rexolite with a dielectric constant of 2.53 and low loss.
Maybe you can mention that it is 3d-printed and designed to mitigate reflection for our range of interest of ~18 to 20 GHz.
I have included the 3d model and a photo of the periodic structure, should people be more interested

## Slide 10: OB200: Technical Feasibility
Piezo controllers
OB200
Laser interferometer
Single motor test rig
ALPS II magnet test stand
Motor velocity with/without B Field
Successful piezo motor tests in cryogenics & inside ALPS II magnet  Motor works in 5.3 T field and at 5 K
Mechanical demonstrator with:
One 200 mm sapphire disk in titanium ring + mirror
Three JPE piezo motors on self-built carriages
Piezo controller system for driving a disk with three motors
interferometer for displacement measurement
arxiv:2305.12808
 Successfully tested at CERN cryolab and at MORPURGO

## Slide 11: Open Booster Calibration
Focusing Mirror
Antenna
Booster
(1 Disk and Mirror)
VNA
x
y
z
Alumina Bead
Mirror
Change in
reflection
coefficient
Boost factor determined using Bead Pull Method (non-resonant perturbation theory) + reciprocity theorem
Electric
field
Beed properties
See poster by Jacob Egge
4

## Slide 12: Open Booster Calibration
Alumina Bead
Mirror
Change in
reflection
coefficient
Electric
field
Beed properties
See poster by Jacob Egge
4

## Slide 13: Signal Power
Measure max. E-field between disk and mirror
Calculate signal power
Includes effects currently not simulated:
  Antenna coupling
  Transverse field perturbations
Single disk “low” boost factor
See poster by Jacob Egge

## Slide 14: OB300: work in progress
Calibration of boost factor with 3 x ⌀ = 300 mm disks
Disks
Rails of disk drive system
Carriages
Laser interferometer couplers
Optical fibres
Tiling of ⌀ = 300 mm LaAlO3 disks
Building mechanical structure for OB300

## Slide 15: MADMAX Prototype
MADMAX Prototype Cryostat (MPC)
LHe reservoir & reliquifiers
Receiver Cryostat (RC)
~4.5 m
Ø < 1.6 m
~3.3 m
Manufactured by Bilfinger Noell GmbH
Two vacuum vessels: - inner (4 K) cooled via LHe circulating through double-wall - outer (isolation vacuum)
Closed-loop system with 4 cryocoolers for reliquification of LHe  during operation: 50 l LHe
Delivery expected begining of 2024
Commissioning with OB300 in Hamburg mid 2024

## Slide 16: MADMAX Staged Program
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
2027
>= 2028
Design Phase
Prototyping Phase
Construction Phase
Foundation of MADMAX Collaboration
DESY PRC
endorsement
OB300 295 K
OB300
1.6T, 4 K
Full-size MADMAX commissioning
Usage of MORPURGO magnet approved by CERN Research Board for 2021-2025
CB100
1.6 T, 295 K
CB100
1.6 T, 4 K
CB200
1.6 T, 295 K
OB300 4 K

## Slide 17: BACKUP

## Slide 18: Coverage

## Slide 19: Dielectric Haloscope
In an external magnetic field the axion field sources an oscillating electric field
is different in materials with different
At the surface, must be continuous
 Emission of electromagnetic waves
Power emitted from a single surface:
for

## Slide 20: Dielectric Haloscope
2 x 104
105
8 x 104
6 x 104
4 x 104
Simulation
In perfect world (1D simulation): achievable with 80 disks and
Non-uniform disk spacing of can achieve broadband response
Tuning of sensitive frequency range by adjusting disk spacing
Area law: ~ const.

## Slide 21: The MADMAX Experiment
MAgnetized Disk and Mirror Axion eXperiment
[Eur. Phys. J. C 79 (2019) 186]
9 T dipole magnet
Booster: adjustable dielectric disks (Ø~1.25 m)
Horn antenna & receiver system
Focusing mirror
Mirror (not visible)
Cryostat (4 K)
~ 1 m

## Slide 22: Designated Experimental Site
DESY
HERA Hall North
MADMAX to be operated at HERA Hall North
Make use of DESY infrastructure  Cryoplatform to be operational in 2025
Benefit: re-use H1 yoke as magnetic shielding
H1 yoke
H1 magnet (to be removed)
H1 yoke
UHH

## Slide 23: Testing the Disk Drive
Project200 successfully tested at CERN Cryolab and in CERN’s Morpurgo magnet
All three piezo motors work at cryogenic temperatures and in 1.6 T field (at RT)
Attocube laser interferometer works at cryogenic temperatures
Project200 backbone structure keeps optics alignment during cool-down
A disk can be moved with three motors using the laser interferometer feedback
Project200 inside Morpurgo
No difference in disk velocity with/without B field

## Slide 24: Axion Like Particle Search
Closed Booster 100
DAQ system
Projected sensitivity
Opportunity to perform ALP search in CERN’s Morpurgo magnet (1.6 T) was used in Mar/Apr 2022
In total 10 h at 1.6 T with ~ 200 K noise temperature
Sensitivity not dominated by RFI in CERN North Hall
Possibilities for an upgrade allowing to cool the setup to < 10 K in Morpurgo currently in preparation

## Slide 25: Dielectric Lens
Rexolite: dielectric constant = 2.53 and low loss
3d-printed and designed to mitigate reflection for our range of interest of ~18 to 20 GHz.
Contact: Anton Ivanov <ivanovan@mpp.mpg.de>

## Slide 26: Receiver Chain
Test setup at MPP with 4 samplers and fake axion injection:
Detection of 1.2 x 10-22 W signal within few days
Low-noise cryogenic amplifier (noise temperature 5 to 6 K)
Receiver chain with low-noise amplifier and three mixing stages
Amplifiers for high frequencies developed: TWPAs for < 30 GHz
Down sampling:
20 GHz  50 MHz
Local oscillators (1 & 2)
Mixers & amps
Samplers
Fake axion injection
LNA

## Slide 27: Cold Calibration Idea
Simulation still missing

## Slide 28: Quantum-limited Amplifier
[Reversed Kerr TWPA arXiv:2101.05815]
Traveling wave parametric amplifier (TWPA)
First 10 GHz TWPA produced (PRX 10, 021021)
Added noise: 1 K above quantum limit (20 dB gain @ 10 GHz)
Future development to 30 GHz

## Slide 29: MADMAX Collaboration Meeting September 2022 @ Hamburg